## Slide 1
Protocol Fuzzing Framework
AI-Driven Multi-Protocol Fuzzer with IDS Evasion & Memory Depletion Attacks
24 Protocols • 100+ Mutation Strategies • 500+ Internal Variants 5-Phase Agentic AI Pipeline • UCB1 Reinforcement Learning • Live FTD Testing
Cisco FTD / Snort 3 — Validated on Real Hardware

## Slide 2
Problem Statement
▸ Modern IDS/IPS (Snort 3, Suricata, Cisco FTD) are trusted to inspect all traffic inline
▸ But deep-packet inspection engines have finite memory pools and CPU budgets
▸ Protocol mutation fuzzing can discover parsing bugs, evasion paths, and resource exhaustion
▸ No existing tool combines: multi-protocol mutation + AI-driven weight tuning + live network delivery + memory depletion attacks + RL adaptation
Goal: Build an automated framework that discovers IDS weaknesses across 24 protocols, tunes attack strategies via AI, and demonstrates real-world inspection bypass on Cisco FTD.

## Slide 3
System Architecture
┌─────────────────────────────────────────────────────────────────────────┐ │ Web Dashboard (Flask + SSE) │ ├────────────┬────────────┬───────────────┬────────────┬─────────────────┤ │ Fuzzer │ AI │ Multi-Proto │ File │ Crash │ │ Control │ Analysis │ Attack │ Send │ Reports │ ├────────────┴────────────┴───────────────┴────────────┴─────────────────┤ │ Fuzzer Engine (main.py) │ │ ┌──────────┐ ┌──────────┐ ┌──────────┐ ┌────────────────────┐ │ │ │ 24 Proto │ │ UCB1 RL │ │ AI Wts │ │ Memory Pressure │ │ │ │ Mutators │ │ Bandit │ │ Engine │ │ TCP Reassembly │ │ │ └──────────┘ └──────────┘ └──────────┘ └────────────────────┘ │ ├────────────────────────────────────────────────────────────────────────┤ │ Transport: PCAP Pipe (local) │ Live Network (TCP/UDP sockets) │ ├────────────────────────────────┴───────────────────────────────────────┤ │ Kali Attacker ──► Cisco FTD (Snort 3 Inline) ──► Target Server │ └────────────────────────────────────────────────────────────────────────┘

## Slide 4
24-Protocol Coverage
Each with dedicated mutation strategies and UCB1 bandit
Transport | Protocols
TCP (13) | DNS, HTTP, HTTP/2, FTP, SMTP, SSH, SMB2, SMB3, DCE/RPC, RTSP, TACACS+, LDAP, Telnet
UDP (9) | DHCP, DHCPv6, SNMP, SIP, MGCP, RADIUS, SUN RPC, TFTP, CIFS/SMB1
ICMP (2) | ICMPv4, ICMPv6
▸ 100+ named strategies across all protocols with 3-7 internal variants each = 500+ unique mutation paths
▸ Strategies target: buffer overflows, state machine violations, reassembly confusion, encoding attacks, protocol desync, fragmentation abuse, compression bombs
▸ File Send: deliver crafted files as properly framed protocol traffic (all 24 protocols)
▸ Custom Payload Mode: inject detection strings (e.g. EICAR) into evasion strategies for testing

## Slide 5
5-Phase Agentic AI Pipeline
Azure OpenAI GPT-5 + Google Gemini backends
Phase | Component | Process | LLM Cost
Phase 1 | Semantic Graph | AST parsing (tree-sitter, 8 languages) → chunking → ChromaDB vector embedding | 0 LLM
Phase 2 | Orchestrator | Repo map → 4K-token chunks → parallel task generation → dedup | N calls
Phase 3 | Explorers | 5 concurrent agents retrieve code via semantic search → vulnerability dossiers | N calls
Phase 4 | Synthesizer | Merge dossiers, deduplicate vulns, extract constants → dynamic_dictionary.json | 0 LLM
Phase 5 | Weigher | Map vulns to strategy weights: Critical=5×, High=3×, Medium=2×, Low=1.5× | 0 LLM
Validated: 2,051 source files → 18,065 AST chunks → 188 explorer tasks → 306 vulnerabilities → 3,295 protocol constants
Resilience: Truncated JSON recovery, ChromaDB index reuse, exponential backoff, chunked orchestration

## Slide 6
Reinforcement Learning — UCB1 Bandit
Real-time strategy adaptation based on observed results
▸ One bandit per protocol — adjusts AI/default weights in real-time
▸ Formula: final_weight = base_weight × rl_multiplier
▸ Crash detected → +0.5× per crash (1 crash = 1.5×, 3 = 2.5×)
▸ No crash, many pulls → slow fade toward 0.5× minimum
▸ Never tried → stays at 1.0× (neutral)
▸ Dashboard shows 4 columns: Original / Applied / RL / Actual
Event | Multiplier | Effect
1 crash | 1.5× | ↑ Weight +50%
3 crashes | 2.5× | ↑ Weight +150%
0 crashes, 100 pulls | ~0.6× | ↓ Weight −40%
Never pulled | 1.0× | No change

## Slide 7
Multi-Protocol Attack Engine
Snort Blinder — Inspector overload via concurrent protocol floods
▸ Launches N parallel snort_blinder.py processes across all 24 protocols
▸ Configurable: duration (up to 3600s), intensity (1-5), process count, protocol selection
▸ 5 Intensity presets with phased escalation (send delays decrease over time)
▸ TCP workers use 30-socket persistent pools with split-segment delivery
▸ Forces Snort to process thousands of concurrent streams across all inspectors simultaneously
▸ FTD SSH monitoring: real-time Snort stats, canary/EICAR detection rate, per-protocol breakdown
▸ Staggered process launch prevents thundering-herd saturation
▸ SO_LINGER(0) on all TCP sockets — prevents TIME_WAIT port exhaustion

## Slide 8
Memory Pressure Mode — TCP Reassembly Attack
Force Snort to hold partial reassembly state across 60+ concurrent streams
▸ Toggle: 'Force TCP Reassembly' checkbox in live mode
▸ 60-socket connection pool per fuzzer instance
▸ Staggered segment delivery: send first half of payload, delay second half by ~60 iterations
▸ Snort must hold partial reassembly buffers for ALL 60 in-flight half-payloads
▸ Each buffer consumes 2560-byte blocks from Snort's memory pool
▸ Multiple instances (4-6 DNS) × 60 sockets = 240-360 partial streams
▸ Exceeds Snort's 201-slot 2560-byte pool → CNT drops to 0
show blocks (FTD)
SIZE MAX LOW CNT FAILED
2560 201 0 0 168467
4096 161 0 1 4339
8192 202 0 3 512
CNT = 0 → Pool exhausted
FAILED = 168,467 allocations denied

## Slide 9
Evasion Testing Results
332 strategies tested against Snort 3 across 23 protocols
Verdict | Count | Percentage
EVADED | 249 | 75.0%
EVADED! (canary undetected) | 50 | 15.1%
DETECTED | 5 | 1.5%
SKIP | 28 | 8.4%
Top EVADED! strategies (canary embedded, Snort blind):
▸ HTTP chunked_confusion (124 B)
▸ HTTP request_smuggling (205 B)
▸ HTTP content_length_attack (99 B)
▸ SMTP mime_decode_bomb
▸ SMB compound_abuse
▸ DCE/RPC fragment_reassembly
90.1% evasion rate — Snort failed to detect embedded canary content in 299/304 testable strategies

## Slide 10
Key Finding: Snort Memory Pool Exhaustion
Demonstrated on real Cisco FTD hardware
▸ Attack: Multi-protocol flood + TCP reassembly pressure depletes Snort's 2560/4096/8192-byte memory pools
▸ Result: CNT → 0 across multiple block sizes, FAILED count reaches 168,000+
▸ Impact: Snort cannot allocate buffers for new packet inspection → packets pass uninspected
▸ Recovery time: 2-5 seconds after attack stops (memory pools refill)
Inspection Bypass Demonstrated:
▸ 10-18 KB of malware data transferred through FTD uninspected during each depletion event
▸ Snort actively blocks the same file (Connection Reset) when memory pools are healthy
▸ Both HTTP and SMB downloads were blocked when healthy, bypassed during depletion
▸ Mid-stream recovery: Snort picks up inspection after ~12 KB → sends RST
▸ Window sufficient for: reverse shells, shellcode stagers, web shells, credential harvesters

## Slide 11
Malware Inspection Bypass — Timeline
Demonstrated with csdl.pdf (358 KB) on Cisco FTD
T=0s
Start multi-protocol flood (intensity 5, 8 processes)
T=3-5s
Snort CNT (2560) drops to 0 — memory pools exhausted
T=5s
Start curl/smbclient download of malware file
T=5-9s
Data flows — 10-18 KB transferred uninspected
T=9-10s
Snort recovers memory, picks up mid-stream inspection
T=10s
Snort detects malware content → Connection Reset (RST)
Baseline
Same file WITHOUT attack → immediate Connection Reset (0 bytes)
Finding
10-18 KB bypass window per depletion event — sufficient for initial payloads

## Slide 12
Network Topology — Dual Deployment
Docker lab for development + Physical Cisco FTD for validation
Docker Lab: Physical FTD: ┌────────────┐ ┌────────────────┐ ┌──────────┐ ┌────────────┐ ┌──────────────┐ ┌──────────┐ │ Kali │───►│ Snort 3 FW │───►│ Target │ │ Kali │───►│ Cisco FTD │───►│ Target │ │ 172.20.0.2 │ │ NFQ Inline │ │172.21.0.2│ │ Attacker │ │ Snort 3 │ │ Server │ │ Port 5000 │ │ 172.20.0.254 │ │ Port 7682│ │ │ │ Inline IPS │ │ │ └────────────┘ └────────────────┘ └──────────┘ └────────────┘ └──────────────┘ └──────────┘
▸ Docker: Snort 3 compiled from source, NFQ DAQ inline mode, checksum_eval='none' for vNIC
▸ FTD: Real Cisco Firepower Threat Defense appliance with production Snort 3 engine
▸ Target: Ubuntu server running vsftpd, dnsmasq, Samba, Apache — real services on all 24 protocol ports
▸ All test results in this presentation from the physical FTD deployment

## Slide 13
Web Dashboard — 5 Integrated Pages
Real-time monitoring via Server-Sent Events (SSE)
Page | Features
Dashboard | Protocol selector (24), pipe/live mode, memory pressure toggle, real-time stats, strategy distribution, event log, multi-instance fuzzing
AI Analysis | Source upload, 5-phase pipeline visualization, vulnerability list, weight apply/reset, analysis history, AI chat for follow-up questions
Multi-Protocol Attack | Protocol grid (All/None/UDP/TCP), target IP, duration/intensity/processes, FTD SSH config, live verdict, per-protocol stats, canary detection bar
File Send | Protocol transport config (24 protocols), file upload, streaming mode with real-time TX/RX hex packet visualization
Crash Reports | List/view/download/delete crash reports with ASan traces, iteration and strategy info

## Slide 14
Technology Stack
Category | Technologies
Backend | Python 3.9+, Flask, SSE, multiprocessing
AI / ML | Azure OpenAI GPT-5, Google Gemini, tree-sitter (8 langs), ChromaDB, tiktoken
RL | UCB1 multi-armed bandit (thread-safe, per-protocol)
Networking | Raw sockets, PCAP pipe, TCP/UDP persistent pools, SO_LINGER, TCP_NODELAY
Protocols | 24 custom binary PDU constructors (DNS, SMB2/3, HTTP/2, DCE/RPC, SIP, etc.)
Monitoring | psutil (local), paramiko/SSH (remote), subprocess oracle
Storage | MongoDB Atlas (conversations), ChromaDB (embeddings)
Infrastructure | Docker Compose, Snort 3 (NFQ DAQ inline), Cisco FTD
Frontend | HTML/CSS/JS dashboard, real-time SSE, hex packet viewer

## Slide 15
Key Results & Conclusions
332 evasion tests
90.1% evasion rate — 50 strategies bypassed Snort with embedded canary undetected
Memory pool exhaustion
CNT → 0 on Cisco FTD; 168,000+ allocation failures across 2560/4096/8192-byte pools
Inspection bypass
10-18 KB malware data transferred uninspected during each depletion event
306 vulnerabilities
Discovered via 5-phase AI pipeline analyzing 2,051 Snort 3 source files
24-protocol coverage
Broadest protocol mutation coverage in a single fuzzing framework
The framework demonstrates that IDS/IPS memory resources are a viable attack surface — finite inspection pools can be exhausted to create bypass windows for malware delivery.

## Slide 16
KEY FINDING: SNORT IPS BYPASS ACHIEVED
Memory block exhaustion causes Snort to fail-open, allowing malware to pass uninspected
2560-BYTE BLOCKS
CNT = 0
1,335,365 FAILED allocations
ATTACK VOLUME
860K PPS
1.72M packets in 2 seconds
BYPASS RESULT
100%
EICAR PDF downloaded intact
FAST-FORWARDED
117 Flows
Packets bypassed Snort entirely
EVIDENCE CHAIN
▸ Baseline: csdl.pdf (350KB) blocked at 4% — Snort detected malware and sent TCP RST
▸ Baseline: eicar-test.txt blocked at 0% — Snort immediately detected EICAR signature
▸ During attack: eicar-adobe-acrobat-attachment.pdf (6,455 bytes) downloaded 100%
▸ MD5 verified: 13486b57cc3ad49227174f86fd4df606 — file integrity intact, no Snort modification
▸ show blocks: 2560-byte CNT=0, LOW=0, FAILED=1,335,365 — DAQ pool completely exhausted
▸ show snort statistics: 117 Fast-Forwarded Flows — LINA bypassed Snort inspection

## Slide 17
BASELINE vs ATTACK: BEFORE & AFTER
WITHOUT FUZZER (Snort Active)
▸ csdl.pdf (350 KB) → blocked at 4%, connection reset by peer
▸ eicar-test.txt (68 bytes) → blocked at 0%, immediate RST
▸ eicar-adobe-acrobat-attachment.pdf → blocked, RST from Snort
▸ All malware signatures detected and blocked
▸ 2560-byte blocks: CNT = 201 (fully available)
WITH FUZZER (Snort Blinded)
▸ eicar-adobe-acrobat-attachment.pdf → 100% downloaded
▸ MD5: 13486b57cc3ad49227174f86fd4df606 ✓
▸ File size: 6,455 bytes — complete and unmodified
▸ Snort never inspected the download flow
▸ 2560-byte blocks: CNT = 0 (completely exhausted)
▸ FAILED allocations: 1,335,365
Conclusion: The fuzzer's multi-protocol flood exhausted LINA's 2560-byte DAQ block pool, forcing the firewall to fail-open. During this window, known malware passed through completely undetected.

## Slide 18
MEMORY BLOCK DEPLETION — show blocks OUTPUT
FTD LINA memory pool status captured during active fuzzer flood
SIZE
MAX
LOW
CNT
FAILED
0
1,450
0
1,450
5,029
4
100
99
100
0
80
1,000
752
980
0
256
4,348
4,213
4,233
0
1550
6,274
1,355
6,261
0
2048
2,100
1,284
2,100
0
2560
201
0
201
1,335,365
4096
161
0
161
33,182
8192
202
0
198
4,392
9344
100
0
100
3,457
16384
100
0
100
7,769
▸ 2560-byte pool (Snort DAQ): LOW=0, CNT reached 0 during attack, 1.3M+ allocation failures ▸ 4096/8192/9344/16384 pools also hit LOW=0 — cascading resource exhaustion ▸ When CNT=0 for 2560, LINA triggers 'snort-blist-full' → fast-forwards all new flows

## Slide 19
SNORT INSPECTION STATISTICS — show snort statistics
PASSED PACKETS
99,287,292
Inspected and allowed
BLOCKED PACKETS
2,550
Malware/exploit detected
FAST-FORWARDED FLOWS
117
Bypassed Snort completely
WHAT THE NUMBERS MEAN
▸ 99.28M packets passed normally — Snort was functional before and after the attack
▸ 2,550 packets blocked — Snort detected malware in baseline tests (csdl.pdf, eicar files)
▸ 117 flows fast-forwarded — These flows BYPASSED Snort entirely due to block exhaustion
▸ The malware download occurred during one of these 117 fast-forwarded flows
▸ Fast-forwarding means LINA sent the traffic directly to the destination without any IPS inspection
▸ TCP Ack bypass: 18,428,575 — shows massive TCP volume from the fuzzer flood

## Slide 20
ATTACK METHODOLOGY — HOW THE BYPASS WORKS
Attack Configuration
▸ 4× DNS instances (High intensity) — TCP SYN flood to port 53
▸ 1× Multi-protocol attack (All 28 protocols) — Max intensity
▸ 12 parallel processes, ~860,000 packets/sec combined
▸ Multi-segment TCP splitting (64-256 byte segments)
▸ IPS trigger patterns embedded in every payload
▸ Aggressive socket rotation (new LINA flow every 5 packets)
▸ 120 concurrent TCP connections per worker thread
Why It Works
▸ LINA has a fixed 201-block pool for Snort DAQ (2560 bytes each)
▸ Each packet sent to Snort allocates one DAQ block
▸ Block is freed only after Snort finishes processing
▸ Parser-based fuzzing forces deep rule evaluation (~10-50μs/pkt)
▸ At 860K PPS, blocks allocate faster than Snort can free them
▸ All 201 blocks occupied → CNT=0 → snort-blist-full
▸ LINA fails OPEN: fast-forwards new flows past Snort

## Slide 21
PACKET CAPTURE — TRAFFIC DURING BYPASS WINDOW
tcpdump capture on eth1 during successful malware download (02:27:34 – 02:27:43 UTC-4)
Protocol Hierarchy (2-second window)
▸ Total: 1,723,306 frames / 2.36 GB in 2 seconds
▸ TCP: 1,718,124 frames (99.7%) — multi-segment flood traffic
▸ ├─ TLS: 298,946 frames — encrypted protocol fuzzing
▸ ├─ SSH: 8,854 frames — SSH protocol fuzzing
▸ └─ HTTP: 1,237 frames — clean HTTP with IPS triggers
▸ UDP: 2,158 frames — DNS (832), DHCP (258), TFTP (48)
▸ ICMP/OSPF/IGMP: 41 frames — additional protocol pressure
DNS Flood Packets (last captured before bypass)
02:27:34.813891 192.168.41.100:45860 → 192.168.42.100:53 [SYN] seq=223513813 02:27:34.813892 192.168.41.100:45858 → 192.168.42.100:53 [SYN] seq=1689849355 02:27:34.813893 192.168.41.100:45872 → 192.168.42.100:53 [SYN] seq=3591821103 02:27:34.816141 192.168.41.100:46170 → 192.168.42.100:53 [SYN] seq=3138697228 02:27:34.816631 192.168.41.100:46230 → 192.168.42.100:53 [SYN] seq=3946152392 ... (33 DNS SYN packets captured in rapid succession — new source port per packet)

## Slide 22
MALWARE DOWNLOAD — PROOF OF BYPASS
FILE DOWNLOADED
eicar-adobe-acrobat-attachment.pdf
EICAR antivirus test file embedded in PDF
MD5 HASH
13486b57cc3ad49227174f86fd4df606
Matches original — file unmodified by Snort
Terminal Output:
root@Kail-00:~# curl -o test_pdf.pdf http://192.168.42.100/files/eicar-adobe-acrobat-attachment.pdf % Total % Received % Xferd Average Speed Time Time Time Current Dload Upload Total Spent Left Speed 100 6455 100 6455 0 0 597.1k 0 0 root@Kail-00:~# ls -la test_pdf.pdf -rw-r--r-- 1 root root 6455 Jun 30 02:50 test_pdf.pdf root@Kail-00:~# md5sum test_pdf.pdf 13486b57cc3ad49227174f86fd4df606 test_pdf.pdf
▸ 100% of file received (6,455 bytes) — Snort did not reset the connection ▸ MD5 hash matches the original file on the server — zero bytes modified

## Slide 23
SECURITY IMPLICATIONS & RECOMMENDATIONS
Vulnerability Identified
▸ Cisco FTD's LINA engine uses fixed-size memory block pools
▸ The 2560-byte pool (Snort DAQ) has only 201 blocks
▸ Sustained multi-protocol flood exhausts the pool
▸ When exhausted, LINA fails OPEN — not closed
▸ New flows bypass Snort entirely (fast-forwarded)
▸ Attacker can deliver malware during the bypass window
▸ No CVE required — this is a design limitation, not a code bug
Recommendations
▸ Implement fail-CLOSED policy when block pools are exhausted
▸ Increase 2560-byte pool size or make it dynamically scalable
▸ Add rate limiting per source IP at the LINA level
▸ Monitor 'snort-blist-full' events and alert SOC teams
▸ Deploy network-level DDoS protection upstream of FTD
▸ Consider redundant IPS in HA for inspection continuity
▸ Implement connection limits per source to prevent SYN floods